## Slide 1: Out of Band Management
HP Lights Out Technology

## Slide 2: Introduction
I own a small consulting company located in NE Portland.
I Have worked for startups, medium and large companies with various hardware and datacenters.
Recently moved from Atlanta, GA
Started as a Unix Admin back in 2003 after graduating with a CS degree.

## Slide 3: Out of Band Management
Involves the use of a dedicated management channel for device maintenance.
It allows a system administrator to monitor and manage servers and other network equipment by remote control regardless of whether the machine is powered on.

## Slide 4: Ilo2 Management Features
Remote power management
Remote media
Hardware watchdog (auto reboot)
Remote Console (with advanced license)
Ssh/telnet/https connectivity
LDAP integration
Ssh key or cert authentication
Online firmware upgrades for ilo
Access to temperature sensors, fan speeds and other sensors
Power consumption usage

## Slide 5: Similar Technologies
DRAC (Dell Remote Access Connection)
iLOM (Sun integrate lights out manager)
IMM (IBM Integrated Management Module)

## Slide 6: Virtual Media
Load a usb, floppy or cdrom image virtually over a LAN/WAN connection.
Can use image from your machine or load from Webdav server.
Support Virtual media scripting (autoload usb keys, change boot options)
Use hplovm to control boot options and connected media

## Slide 7: IPMI
Out-of-band management standard created by Intel
Was supposed to allow users control a heterogeneous environment with one tool
Supports
  power control
  SOL (Serial over LAN)
  virtual media
  Access to thermal and fan sensors
  Hardware watchdog
  Access Hardware Logs
Manufactures don’t abide by the standard 100%
IPMI BMC shares connection with Ethernet port

## Slide 8: Sensor Information

## Slide 9: IML

## Slide 10: Quick status and UID Light

## Slide 11: Share network Port

## Slide 12: Ilo3
Bigger, faster, better
Uses JSON
As fast or faster than KVM console
800% faster than ilo2
Management device runs linux (of course)
Remote console built into .Net framework for windows
Jave interface for non-windows users

## Slide 13: Advanced iLO3
Dynamic Power Capping
Phase shedding (Voltage Regulator)
Power profiles
Power Consumption usage (snmp section enabled)
License required ($300)

## Slide 14: Advanced ilo Topics
SSH Key Authentication
LDAP or AD Authentication
Certificate Authentication

## Slide 15: Server Power Controls

## Slide 16: Deploying ilo
Basic workflow for deploying ilo:
Get unique password for each system (as the default)
Plug ethernet cable in to ilo port
Use nmap to find unique ilo-serial dns name
Goto http://ilo-ip
Enter unique password and configure from web console
Repeat for each server you have

## Slide 17: Scripting Toolkit and RIBCL
XML Language used to configure ilo2 interfaces
<RIBCL VERSION="2.0">
<LOGIN USER_LOGIN="adminname" PASSWORD="password">
<SERVER_INFO MODE="write">
<SERVER_NAME value ="${HOST}"/>
</SERVER_INFO>
<RIB_INFO MODE="write">
<MOD_NETWORK_SETTINGS>
<REG_DDNS_SERVER value="Yes"/>
<DHCP_DOMAIN_NAME value="Yes"/>
<DHCP_ENABLE value="Yes"/>
<DNS_NAME value="ilo-${HOST}"/>
<DHCP_GATEWAY value="Yes"/>
<DHCP_DNS_SERVER value="Yes"/>
<DHCP_WINS_SERVER value="Yes"/>
<DHCP_STATIC_ROUTE value="Yes"/>
</MOD_NETWORK_SETTINGS>
</RIB_INFO>
</RIBCL>

## Slide 18: Automating ilo Deployment
Install Proliant Support Pack (you need this regardless)
  See readme before installing in your environment (HP likes to compile drivers for you)
    Your Lpfc devices will disappear on RHEL 5.5+ and RHEL6
  Make sure hponfig, hp-health and ilo device driver are installed
  Write a XML file using the RIBCL XML Definations
  Use hponfig to configure your ilo from the command line (no password needed!)
  Send XML over https if you know the password
  User your favorite language to automate sending XML over https

## Slide 19: hponfig
Upgrade ilo firmware
Write current config in RIBCL
Upload RIBCL script to configure your ilo
NO PASSWORD NEEDED

## Slide 20: Ilo Type for puppet
Very possible to create type in order to automate your ilo deployment.
Hponfig would be the provider. However, https can also be used.
ilo { “ilo2.0”:
  ribclversion => “2.0”,
  provider => “hponfig”,
  hponfigpath => “/opt/hp/hponfig”
  username => admin,
  password => shhh_secret,
  shared_network => true,
  usedhcp =>true,
  ip => “${someip},
  }

## Slide 21: Trade Secrets
Get a 60 day eval Advanced ilo license if you need Remote console.
Update your ilo firmware from the OS, SIM, or SMH
Might be able to use the shared network port feature
Use Static address
Stick on separate network / VLAN (Management Network)
Older ilos don’t support newer RIBCL commands

## Slide 22: Helpful Links
ilo3
http://h20000.www2.hp.com/bc/docs/support/SupportManual/c00190541/c00190541.pdf
ilo2
http://h20000.www2.hp.com/bc/docs/support/SupportManual/c00553302/c00553302.pdf
Ilo2 Active Directory integration
http://www.techietips.net/Configure-Windows-ADS-Authentication-for-HP-iLO-2-card
HP Insight Foundation Page
http://h18004.www1.hp.com/products/servers/management/core-management-100.html

## Slide 23: Contact and Source Code
Corey Osman – corey@logicminds.biz
git://github.com/logicminds/devops.git

## Slide 24: Questions
?